Cascade embedded learning for Human Activity Recognition.

Abstract :- This project uses ensemble technique of Cascade Ensemble Learning(CEL) with stacking for classification of Human Activity Recognition(HAR) dataset. Each layer of Cascade Ensemble Learning has KNN, Logistic Regression and SVM classifiers. Probability of each class is calculated from KNN, Logistic Regression and SVM classifers which is stacked to the input data and it is passed to the next layer as input. HAR data set has data of triaxial acceleration from accelerometer and triaxial angular velocity from gyroscope. HAR data set has 561 features for 6 class labels as WALKING, WALKING_UPSTAIRS, WALKING_DOWNSTAIRS, SITTING, STANDING, LAYING.

Data set preprocessing :-
HAR data set has 10,299 data points and 561 features. Working with such a large data set can be compuationaly intensive and can lead complex and over fitted model. Principal component analysis(PCA) is used for dimensionality reduction. Table 1 shows explained variance ratio for different number of PCA components. CEL model is trained for PCA components given in table and results are discussed.

Number of PCA components	Number of PCA components = 10	Number of PCA components = 20	Number of PCA components = 30	Number of PCA components = 40	Number of PCA components = 50	Number of PCA components = 70	Number of PCA components = 100
Explained variance ratio	0.8050	0.8578	0.89	0.91	0.93	0.95	0.99

Cascade ensemble learning technique:-
CEL is based on the idea that different models will misclasify different samples and combining the results of these classifiers can have better recoginition rate.
CEL model has SVM, KNN and logistic regression classifers. In CEL model, class probability vector predicted from the the present layer is concatinated in the input data of the layer which is considered as input to the next layer. Class probability vectors are calculated by using stacking technique which is explained next.

Stacking:- Training data set is split into 10 parts. Classifier is fitted on 9 parts and probability vectors is generated for 10th part and this is repeated for every part. Probability vectors of each classifiers are added as features to the training data. This new training data is passed to the next layer for prediction.

10 fold cross validation is used to calculate the recoginition rate of the models.

--> little bit about data set
--> stacking technique
data pre processing --> Dim reduction
1. PCA
2.

Results --> 10 times 10 fold cross validation

		KNN	Logistic Regression	SVM	Cascade embedded Learning
Number of components in PCA = 40 / Number of Layers = 2		0.8946	0.923	0.9240	0.9652
					0.00047
Number of components in PCA = 70 / Number of Layers = 2		0.9102	0.9458	0.9447	0.9650
					0.00047
Number of components in PCA = 40 / Number of Layers = 3		0.8946	0.923	0.9240	0.9642
					0.0005
Number of components in PCA = 100 / Number of Layers = 2		0.9141	0.9618	0.9620	Mean: 0.9898051647843603 Variance 3.8130288058906564e-06
Number of components in PCA = 70 / Number of Layers = 2		0.9094	0.9462	0.9432	Mean: 0.9821346957645749 Variance 7.942661937877455e-06
Number of components in PCA = 50 / Number of Layers = 2		0.9025	0.9291	0.9280	Mean: 0.976018002207818 Variance 1.5441360393347608e-05
Number of components in PCA = 40 / Number of Layers = 2		0.8947	0.9232	0.9254	Mean: 0.9698039382188381 Variance 2.1158342267313026e-05
Number of components in PCA = 30 / Number of Layers = 2		0.8907	0.9066	0.9064	Mean: 0.9584434883523452 Variance 3.195139543841608e-05
Number of components in PCA = 20 / Number of Layers = 2		0.8807	0.8962	0.8972	0.9426
Number of components in PCA = 10 / Number of Layers = 2		0.8561	0.8782	0.8831	0.9130

Number of PCA components	Number of PCA components = 10	Number of PCA components = 20	Number of PCA components = 30	Number of PCA components = 40	Number of PCA components = 70	Number of PCA components = 100
Explained variance ratio	0.8050	0.8578	0.89	0.91	0.95	0.99